## Slide 1: Profiling Code for Execution Time

## Slide 2: Overview
Which part of the code uses the most time?
That’s the best place to start optimization for speed, as it has the largest impact

## Slide 3: Sampling a Program
Keep an array of counter variables, one per function
Periodically sample the program as it runs
  Find which function is running
  Increment the counter variable for that function
After run, examine the counter array to see which functions dominate execution time
Where are you now? What are you doing?
Activity | Count
Studying calculus | 37
Walking/biking/rollerblading | 12
Soldering | 7
Writing code | 55
Eating | 5
Study break | 6
Sleeping | 14

## Slide 4: Making the Program Self-Sampling
Want target program to monitor itself
Periodically samples itself as it runs
  Trigger PC sampling with a timer interrupt
  See which function was running by finding the ISR’s return address
  Increment the counter variable for that function
Target program needs data structures:
  Address-to-function translation table
  Execution count for each region
Need a helper program to generate address-to-function translation table and integrate into application’s source code
Where am I now? What am I doing?

## Slide 5: Data Flow for Profiling Support
Executable file holds symbol table with addresses of all functions
Helper program examines executable to make a C file which declares and initializes the region table.
Then rebuild program using updated region table
Get Regions

## Slide 6: Region Information
Target program needs an array to use (while running) to translate an address to a function name
Getregions program
  Analyzes .axf file to find function names, starting addresses and lengths
  Generates C code to define and initialize an array of REGION_T elements
Each function is described by an entry in RegionTable
  Start: first address used by this region
  End: last address used by this region
  Region name: simplifies analysis
Place table in ROM (using const) to save RAM space

## Slide 7: Additional Profile Information
Region count information
  RegionCount
  Placed in RAM
  Updated by ISR during sampling, so declare as volatile
NumProfileRegions
  Total number of regions in table
Number of samples taken
  profile_ticks
Flag controlling profiling
  profiling_enabled
Number of addresses which couldn’t be found in region table
Last address which wasn’t found
Profile.c
Region.c

## Slide 8: Extracting function addresses from executable

## Slide 9: Finding Function Addresses
MDK creates executable image with .axf extension
  Format of .axf file is ELF (Executable and Linkable Format)
  http://man7.org/linux/man-pages/man5/elf.5.html
Example sections
  .text: executable program instructions (machine code)
  .data: initialized data
  .bss: uninitialized data (actually cleared to zero)
  .symtab: symbol table for debugging
  .strtab: string table with names of sections and symbols
Symbol Table
  Holds information for each symbol (e.g. function)
    st_value: beginning address of symbol
    st_size: size of symbol
    st_name: location of symbol’s name in string table
Image: Wikipedia

## Slide 10: Using Getregion
Build your program in uVision.
Run update_regions_manually.bat (in the Scripts folder) to create a new region.c file (which is placed in the src folder). This file will have the correct number of entries but the addresses may be wrong (this is ok – a later pass will fix this).
Rebuild your program in uVision to generate an executable with the correct size region table. Note that this table still uses the old function addresses, which will be wrong if the previous region table had a different number of entries.
Run update_regions_manually.bat to create a new region.c file with the correct function addresses and the correct number of entries.
Rebuild your program in mVision to generate an executable with the correct region addresses.
Download and execute your program on the target hardware. This will populate the RegionCount table to indicate the execution time profile.

## Slide 11: Retrieving the Return Address and finding the function

## Slide 12: Identifying the Interrupted Function
Demo code uses PIT to generate periodic interrupt
Within timer ISR:
  Read the return address from the stack
  Examine table of region addresses to determine currently executing region i
  Increment entry i of execution count table
  Extras
    Increment a total number of ticks variable (to reveal out-of-range PC instances) – want to be able to double-check the measurements
    Keep track of last address which was not found

## Slide 13: Finding Return Address in ISR
Where is the return address stored?
  Not in LR – that holds an exception return code in ISRs
  Instead need to access saved PC value on stack
Where is it on the stack?
  Offset from SP depends on when we access it, since SP changes
2. SP points here upon entering ISR
ISR stack frame contents
3. SP points here at start of ISR function body
1. SP points here before interrupt

## Slide 14: Finding Return Address in ISR
Can’t use intrinsic __return_address()
  Returns value of link register, used to return from subroutine calls, not ISRs
Instead read saved PC value from stack
  Use compiler’s __current_sp() intrinsic to read current value of SP
  Add offset for context saved by hardware in response to interrupt (RET_ADX_OFFSET)
  Add offset for ISR’s additional stack frame contents (CUR_FRAME_SIZE)
  Load the word from resulting memory address
Resulting object code
  Look at what that long line of C code turned into! Very efficient object code.
Define constant values in profile.h
  RET_ADX_OFFSET = 0x18
  CUR_FRAME_SIZE = ? -> Need to compile function and inspect object code

## Slide 15: Object Code Inspection
Look for instructions (between ISR entry and return address calculation) which modify stack pointer
  PUSH, POP, changes to sp (r13))
Determine how each instruction modifies the stack pointer
  PUSH {r4,r5}
  pushes 2*4 bytes, so set CUR_FRAME_SIZE to 8
;;;15 void PIT_IRQHandler() {
000000 b430 PUSH {r4,r5}
000002 2001 MOVS r0,#1
000004 4955 LDR r1,|L1.348|
000006 0580 LSLS r0,r0,#22
000008 6008 STR r0,[r1,#0]
00000a 4855 LDR r0,|L1.352|
00000c 68c1 LDR r1,[r0,#0xc]
00000e 07c9 LSLS r1,r1,#31
000010 d032 BEQ |L1.120|
000012 68c1 LDR r1,[r0,#0xc]
000014 07c9 LSLS r1,r1,#31
000016 0fc9 LSRS r1,r1,#31
000018 60c1 STR r1,[r0,#0xc]
00001a 4852 LDR r0,|L1.356|
00001c 7800 LDRB r0,[r0,#0]
00001e 2800 CMP r0,#0
000020 d028 BEQ |L1.116|
;;;30 PC_val = *((unsigned int *) (__current_sp()+CUR_FRAME_SIZE+RET_ADX_OFFSET));
000022 4668 MOV r0,sp
000024 6a01 LDR r1,[r0,#0x20]

## Slide 16: Looking Up The Address
This function executes frequently and should be optimized
Could sort entries, starting with most frequently executed regions
  “Profile-driven profiler optimization!”
Uses a linear search
  Change to binary search? Need to sort regions in address order

## Slide 17: Demonstration

## Slide 18: Profiler API and Use
void Init_Profiling(void)
  Clears RegionCount table
  Initializes and starts timer
void Disable_Profiling(void)
  Clears profiling_enabled flag
void Enable_Profiling(void)
  Sets profiling_enabled flag
Program responsibilities
  Initialize profiling system and timers with Init_Profiling()
  Ensure interrupts are enabled with __enable_irq()
  Enable profiling
  Run code in question
  Disable profiling

## Slide 19: Build Sequence
Build the program using a dummy region.c file. Region.c has wrong number of regions, wrong addresses.
Run tool to create the region table from the executable. Region.c has right number of regions, but wrong addresses.
Rebuild the program. The resulting executable symbol table has the correct function addresses.
Run tool to create the region table from the executable. Region.c has right number of regions, right addresses.
Rebuild the program. Executable’s region table has right number of regions, right addresses
Get Regions

## Slide 20: ProfileDemo
Where does this program spend most of its time?
  f1, f2 and f3 are floats
Each loop has
  2 FP adds
  2 FP multiplies
  1 FP sine
  1 FP cosine
Build program, download, run
Break at while (1) loop
Examine RegionCount and profile_ticks

## Slide 21: Disadvantages of Sampling
Sampling is inexact - not guaranteed to get everything that runs
  Code which disables interrupts (e.g. ISRs, OS code) is not measured
  Rarely executed code may be missed
  Takes time for numbers to settle down
  Profile changes based on mode of program
How long is enough?
  The statistician I asked said “Well, it depends,” and changed the subject
  A complex statistical question!
    If this were a statistics class, we probably would never actually get to running the program…
  So, run it until the digits you care about stop changing.
    9%? 9.7%? 9.73%? 9.731%? 9.731123452345245%?
    Each additional digit will take more time to stabilize

## Slide 22: Results
profile_ticks = 5329 (number of samples)
Top region is #26
  1413 samples/5329 = 26.5%
  Look up #26 in RegionTable – is _aeabi_fmul (floating-point multiply)
2nd region is #23
  1345 / 5329 = 25.2%
  __aeabi_fadd (fp add)
3rd region is #39
  494 / 5329 = 9.3%
  __mathlib_rredf2 (?)
RegionCount
RegionTable

## Slide 23: How long do the sin and cos calls take?
Look them up in RegionTable
  Entries 45 (sinf) and 44 (cosf)
Then look in RegionCount
  Sinf: 264/5329 = 4.95%
  Cosf: 248/5329 = 4.64%
Are those functions really that fast? 2.5x faster than multiply or add?
  No they aren’t!
  Look at object code for sinf in disassembly window
  Many calls to fmul and other functions
RegionCount
RegionTable
sinf Disassembly

## Slide 24: Flat vs. Cumulative Profile
Flat profile
  A function F accumulates time only if the PC address sample is in function F
Cumulative profile
  A function F accumulates time
    If the PC address sample is in function F
    If the PC address sample is in a function G, which F called (directly or indirectly)
      All functions above G in the call tree also accumulate time
  This can be done by examining all return addresses on the call stack
    Not implemented here
    Extra credit project!
Approximation
  Modify function of interest to set an output bit on entry, clear it on exit
  Examine bit with oscilloscope, measure duty cycle
sinf
fmul
frnd
f2iz
fmul
frsub
fsub
rredf2